## Slide 2: FRC Training #2 Agenda:
Drive Systems, Wheels, Motors
Robot Arms, Belts/Pulleys, Pneumatics
Robotic Control, Sensors, Feedback
Autonomy, Remote Control, Situational Awareness
Case Study: Design Your Robot!

## Slide 3: First, a little physics…
Force = m * a
Power = V * I
21 in-lb Torque
2600 RPM
12V Lead-Acid
17.2 Amp-Hours
Power =
Torque * RPM * (Constant)

## Slide 4: FRC Wheels
Omni Wheel
High-Traction
Slick Wheel
Treads
Casters
Mecanum

## Slide 5: FRC Drivetrains

## Slide 6: FRC Drivetrains

## Slide 7: Drivetrain Things to Consider
Number, Type, and Size of Wheels
Drive (powered) vs Guide (unpowered)
Wide-body or Narrow-body Chassis
One or multiple wheels per motor
Gear and Chain Ratios
Transmission?

## Slide 8: Robot Control: Output
Speed Controllers
Regulate Voltage to Motors
Accepts a “Pulse Width Modulated” (PWM) output from cRio Controller
0% Duty cycle = no power
100% duty cycle = full power

## Slide 9: Robot Control: Output
Relays
Full ON (forwards or backwards) or Full OFF

## Slide 10: Robot Control: Input
Potentiometer
Optical encoder

## Slide 11: Robot Control: Input
Limit Switch:
Can determine if arm reaches max distance/hard stop
Gyroscope:
Determine direction robot is pointing

## Slide 12: Robot Control: Input
Microsoft Kinect:
3D Imaging and Light Detection
Infrared/Laser Sensor:
Can determine if an object passed in between sensor + transmitter

## Slide 13: Remote Control
Joystick
Controller
Dashboard

## Slide 14
Robot Sequencing

## Slide 15
What I Do as a Rocket Scientist – (aka the “day job”)
Spin around!

## Slide 16
What I Do as a Rocket Scientist – (aka the “day job”)
How’d I do??

## Slide 17
(It’s not quite that simple)
Enable thrusters
Configure spin rate
Switch gainsets
Enable solar array sun tracking
Enable omni antenna
Configure thermal heaters
Update mass properties
Desaturate momentum wheels
Update gyro attitude
Lots of commands!
??? I’m confused… FAULT!

## Slide 18
Autonomous Mode
Holy Cows Video
Its all about the sequencing!
Step 1: Arm down + move backward
Step 2: Move forward 6 feet
Step 3: Raise Arm to scoring angle
Step 4: Launch discs
Step 5: Arm down + move backward
Step 6: Turn on disc pickup
Step 7: Drive forward 6 feet
Step 8: Turn off disc pickup
Step 9: Arm up to scoring angle + move backward
Step 10: Launch discs

## Slide 19: Robot Autonomy
Situation:
  Robot arm needs to pick up game piece on ground, then rotate 50 degrees upward to place on rack
Introducing Closed-Loop Control
Proportional – Integral – Derivative “PID” Control
  How do we stop arm at 50 degrees?
    Potentiometer will tell you position…
    … But that’s not enough

## Slide 20: Robot Control
Proportional:
How far away is the desired angle?
Derivative:
How fast am I moving towards the desired angle?
Integral:
How far have I already moved?

## Slide 21: Robot Control
Proportional:
Faster when further away
Output = Kp * Δθ
Derivative:
Slows down when getting close (“Dampens”)
Output = Kd * ω
Integral:
Reduces “steady state” error
Output = Ki * θ * Δt
These are known as “GAINS”

## Slide 22
Moving from vertical to horizontal
This arm starts out SOOOOOO SLOW!!!
Notes: Poll Title: What should you do? http://www.polleverywhere.com/multiple_choice_polls/al5GI7B4pnIh0ko

## Slide 23
I wanna shoot here
But my arm always ends up here!
Notes: Poll Title: What should you do? http://www.polleverywhere.com/multiple_choice_polls/ieE7e61rSirtI8n

## Slide 24: Robot Autonomy
Situation:
  Robot is 30 feet away, need to move sideways to pick up game piece
  How do we move straight if you can’t see the robot?
    Encoders will tell you how far each wheel moved…
    …But that’s not enough
Introducing Motor Drive Boost!

## Slide 25: Robot Control
Applying same motor power follows “actual path”
Difference in motor efficiency, gearbox friction, chain tension, misalignment
Must modify motor power based on feedback to move straight